Webpage specific functionality

## Relay Controls
suggested widget: toggle buttons
Path: api/v1/relays

POST
switch0	0-1
switch1	0-1

GET
switch0	0-1
switch1	0-1

## Timers
suggested widget: apple app
Path: api/v1/timers

POST
active	0-1
hour	0-59
min	0-59
sec	0-59
repeat	7 bit number (1 bit for each day mon-sun)
action	on/off/toggle (0,1,2)

GET
active	0-1
hour	0-59
min	0-59
sec	0-59
repeat	7 bit number (1 bit for each day mon-sun)
action	on/off/toggle (0,1,2)

## Clock
The server will attempt to grab the current time from world time api: http://worldtimeapi.org/
If the user is not connected to the internet then it should have a widget appear that allows the user to set the current time.
If time is 0, it means that microcontroller has been reset.
Widget: Only allow clock setting if GET command upon load in
Path: api/v1/clock
POST
Unix time	integer

GET
Unix time	integer

## Power Reporting
suggested widget: A graph and a drop down for the time period
Path: api/v1/power_monitor

GET
time_period	hour/3 hours/6 hours/12 hours/24 hours
data	array of 60 data points

## Debugging
suggested widget: A push button and then a warning box

Path: api/v1/reset_device
reset	boolean

Actions:
- Upon page load all of the GET commands will run and populate the widget
- The user will be able to configure and save each timer. I want this to be similar to the apple alarm app.
- The user will be able to toggle the relay switches individually.